## Slide 1: Peltan Christian Primary School Perimeter Walls
Background: The current primary concern for the school is the lack of security. The addition of perimeter walls around the school grounds gives the school the security that they feel necessary to continue forward with further school improvements such as the possible implementation
of solar power.
Objectives:
Provide Security
  Needs to be approx. 8 ft tall
  Topped with broken glass
Safe/Appropriate Construction
  Built to withstand earthquakes/weather
  Built with appropriate standards –not over/under designed
Findings/Solutions:
Conversed with
Scott Michaels -local US contractor, builds CMU walls in houses, etc.
Carl Garner -soil engineer, knowledgeable about walls, and any other structure, has worked in Haiti
Don Johnson -works Haiti Outreach, familiar with local materials and building code/techniques
Gained confidence in footer dimensions
Gained knowledge about CMU construction techniques and availability of certain material in Haiti

## Slide 2: Footer
Most literature suggests that the depth and width of the footer should be approx. twice the width of the CMU
S. Michaels and C. Garner suggested this was an appropriate amount and that the soil was adequate for this
S. Michaels mentioned running 4 lengths of rebar in footer which ties into vertical rebar
Footer along columns (if columns are larger than the wall width) should be approx. 6-8” greater on either side

## Slide 3: Body
Walls need vertical supports
Typical Haitian wall construction usually has a concrete column every 10 to 12 feet or so (column consists of 4 vertical rebar
Scott Michaels suggested using a single vertical rebar inside a filled core of a CMU block every 3-4 ft
Vertical supports need to be tied into the footer and bond beam
C. Garner suggested the use of truss wire that can be placed after every three bricks or so for horizontal strength

## Slide 4: Bond Beam
A bond beam is necessary to tie all of the vertical rebar together
Scott Michaels suggest running 2 rebar along the top
Don Johnson didn’t think that bond beam blocks would be accessible
Bond beam blocks can be made from modifying typical CMUs
Typical Haiti construction pours bond beam without blocks